SECTION 10260

SMARTRAIL

PART 1  GENERAL

1.01 SECTION INCLUDES

A. 5 1/2" Spectrim SmartRail.

1.02 SUBMITTALS

A. Comply with the requirements of Section 001300- Submittals.

B. Product Data: Submit manufacturers product data.

C. Shop Drawings: Submit Shop Drawings showing Components, dimensions. And anchorage details.

D. Samples: Submit 12" (304.8 mm) long sample of each model and color specified, including end caps and internal components for architect’s approval.

E. Certification: Submit manufacturer’s certification indicating compliance with ADA requirements.

1.03 QUALITY ASSURANCE

A. Comply with NFPA 101 for interior finished materials.  Smoke developed less than 450 and flame spread of 25 or less in accordance with ASTM E84.

1.04 DELIVERY, STORAGE, AND HANDLING

A. Delivery: Deliver materials to site in manufacturer’s original, unopened containers and packaging with labels clearly indicating manufacturer of material.

B. Storage: Store materials indoors in a clean, dry area protected from damage and in accordance with manufacturer’s instructions.

C. Handling: Protect materials during handling and installation to prevent damage.

PART 2  PRODUCTS

2.01 MANUFACTURER

A. Spectrim Building Products, LLC

3433 Marshall Lane

Bensalem, PA 19020

www.spectrimbp.com

P: 215-245-4210

2.02 SMARTRAIL

A. Spectrim SmartRail: SmartRail aluminum cylinder and aluminum channel.

1. Horizontal Insert: Finish - Acrylic Silverspun (12 mm)

2. Aluminum Top Grab Rail and Bottom Channel:  Finish- Bengal Silver powder coat

3. Stand Off Bracket: Finish - Clear acrylic

4. Decorative Bolt Cover Caps: Finish – Satin Chrome

PART 3 EXECUTION

3.01 EXAMINATION

A. Inspect wall surfaces to receive SmartRail.  Notify the Architect in writing if wall surfaces are not acceptable.  Do not begin installation until unacceptable conditions have been corrected.

3.02 INSTALLATION

A. Install SmartRail to wall securely and in accordance with manufacturer’s written instructions.

B. Install SmartRail accurately in location, alignment ad elevation.

C. Provide steel stud back-up in drywall stud cavity to accept fasteners.